## Slide 1
UNIVERSITY OF AGDER
MAS512 Assignment 2
Group 9
Camera Geometry
LiDAR Tracking
Sensor Fusion
Navigation
By:
Renwa Hamid
Sebastian Skogland
Hedda Winther-Sørensen
MAS512 | Assignment 2 | Group 9
1

## Slide 2
Assignment 2 — Our workflow
From camera-based tracking to LiDAR, sensor fusion and autonomous control
MAS512 | Assignment 2 | Group 9
2
Q1
Camera
3D trajectory, camera intrinsics and coordinate mapping
Q2
LiDAR
Point-cloud clustering, load motion and KISS-ICP
Q3
Camera–LiDAR
KITTI calibration, 3D ranging and validation
Q4
Webots
Waypoint control, wheel slip and sensor logging
Assignment 1 models are reused where relevant; results shown in this deck come from the Assignment 2 notebook.

## Slide 3
Q1
Q1(a) Camera → 3D coordinates
Reuse the Assignment 1 YOLO model to reconstruct the swinging-load trajectory
MAS512 | Assignment 2 | Group 9
3
1
RGB + depth
Match 900 RGB images with their aligned raw depth frames.
2
YOLO detection
Predict the load bounding box and calculate its center (u, v).
3
Depth sampling
Read depth at center; use nearest valid pixel in box if missing.
4
3D conversion
Apply focal lengths and principal point from the intrinsic matrix.
Pinhole camera model
X = (u − cₓ) · Z / fₓ
Y = (v − cᵧ) · Z / fᵧ Z = depth [m]
Aligned RGB and depth pixels are combined to obtain camera-frame XYZ coordinates.
900
RGB + depth pairs
889
Load detections
11 frames with no YOLO detection
3D positions were created for detected frames.

## Slide 4
Q1
Q1(a) Depth handling and filtering
Missing center depth and measurement spikes are handled before 3D reconstruction
MAS512 | Assignment 2 | Group 9
4
Measured depth vs cleaned depth
336 → 0
Missing depths among detected frames¹
70
Corrected depth samples
How it works
Nearest valid depth in YOLO box → 7-sample local median → flag deviations > 0.5 m → interpolate.
¹ For 889 detected frames; undetected frames are not included.

## Slide 5
Q1
Q1(a–b) 3D trajectories — two camera matrices
The same detected pixels and cleaned depth values give different XYZ positions
MAS512 | Assignment 2 | Group 9
5
o₁ using lab matrix M_int
o₂ using default matrix M_d
Example o₁ = (−1.805, −1.008, 4.384) m
Example o₂ = (0.265, −0.046, 4.384) m

## Slide 6
Q1
Q1(c) Which intrinsic matrix fits the frames?
Compare principal points and focal lengths for the 640 × 480 images
MAS512 | Assignment 2 | Group 9
6
M_int · Lab calibration
[ 1391.7 0 979.1 ]
[ 0 1388.5 540.2 ]
[ 0 0 1 ]
M_d · Default L515
[ 1342 0 325 ]
[ 0 1342 235 ]
[ 0 0 1 ]
(320, 240)
Approx. frame center
(979, 540)
M_int principal point
(325, 235)
M_d principal point
Conclusion
M_d appears more suitable
Plausibility based on image geometry, not an independent 3D ground-truth test.

## Slide 7
Q1
Q1(d) Learning the coordinate mapping
Linear regression predicts o₂* from o₁ coordinates
MAS512 | Assignment 2 | Group 9
7
INPUT
o₁ = [X, Y, Z]
→
MODEL
Linear Regression
→
OUTPUT
o₂* = predicted XYZ
711
Training samples
178
Test samples
1.000
Test R²
≈ 0
RMSE (7.61 × 10⁻¹⁶)
Near-perfect prediction is expected: both 3D outputs are computed from the same pixels and depths with different matrices.

## Slide 8
Q1
Q1(e) Euclidean coordinate differences
Compare direct matrix conversion and the regression-predicted coordinates
MAS512 | Assignment 2 | Group 9
8
Mean Euclidean distance [m]
o₁ vs o₂
1.718 m
o₁ vs o₂* (test)
1.713 m
Lower is not necessarily better here: this is a difference between coordinate definitions, not ground-truth position error.
1.189–2.610 m
o₁ versus o₂ · min–max
1.293–2.281 m
o₁ versus predicted o₂* · min–max
Interpretation
The two means are similar because regression reproduces o₂ very closely.

## Slide 9
Q2
Q2(a) LiDAR swinging-load tracking
Ouster OS-1 point clouds → DBSCAN clusters → load centroid trajectory
MAS512 | Assignment 2 | Group 9
9
1
Decode scans
Use Ouster metadata + complete scans
2
Crop 3D region
Keep plausible load points
3
DBSCAN
Find compact moving cluster
4
Track centroid
Mean XYZ across scans
Tracked load centroid (3D)
99 complete scans
99/99 clusters detected

## Slide 10
Q2
Q2(a) Load motion over time
XYZ centroid positions reveal repeated swinging motion
MAS512 | Assignment 2 | Group 9
10
Measured centroid coordinates
0.785 m
Y-coordinate span
Observed ranges
X [m]
0.643–0.783
Y [m]
1.354–2.139
Z [m]
0.157–0.231

## Slide 11
Q2
Q2(b) KISS-ICP — sensor motion vs load motion
ICP estimates LiDAR sensor poses; DBSCAN tracks the moving object
MAS512 | Assignment 2 | Group 9
11
KISS-ICP: sensor trajectory
Load in first-scan reference frame
0.0046 m
Max sensor translation
0.0191°
Max sensor rotation
Near-zero sensor motion ≠ stationary load

## Slide 12
Q3
Q3(a) KITTI dataset and calibration
Combine synchronized camera images, LiDAR scans and 3D labels
MAS512 | Assignment 2 | Group 9
12
Example: annotated KITTI subset
Files aligned by frame ID
image_2/
RGB camera images
velodyne/
XYZ + reflectance point clouds
calib/
P2, R0_rect, Tr_velo_to_cam
label_2/
Object labels and 3D locations
Coordinate transformation
LiDAR XYZ → Tr_velo_to_cam → R0_rect → P2 → image pixel (u, v)
Local 2D YOLO subset: 150 train + 40 val images; 5 separate KITTI 3D frames used for paired sensor fusion.

## Slide 13
Q3
Q3 Camera–LiDAR fusion in five KITTI frames
Projected LiDAR points are overlaid with YOLO boxes and distance estimates
MAS512 | Assignment 2 | Group 9
13
000004 · IoU 0.93 · 40.06 m
000008 · IoU 0.86 · 32.57 m
000019 · IoU 0.92 · 8.91 m
000027 · IoU 0.87 · 12.90 m
Green = YOLO prediction · Cyan dashed = matched KITTI 2D label · Point colors represent LiDAR range.

## Slide 14
Q3
Q3 Fusion range validation
Compare LiDAR-estimated object range to matched KITTI 3D annotations
MAS512 | Assignment 2 | Group 9
14
4 / 5
Matched 2D detections
1.82 m
Matched range MAE
0.50
Minimum match IoU
Frame
Box IoU
LiDAR [m]
GT [m]
|Error| [m]
000004
0.93
40.06
41.67
1.61
000008
0.86
32.57
34.29
1.71
000019
0.92
8.91
10.53
1.62
000027
0.87
12.90
15.24
2.34
000029
0.00
22.77
—
—
Unmatched example
Frame 000029
Excluded from error average
Range estimate = 20th percentile of projected LiDAR points in the YOLO box; GT range is to the labeled 3D object location.

## Slide 15
Q4
Q4(a) Webots navigation setup
A Supervisor controller follows a fixed route and records repeatable friction experiments
MAS512 | Assignment 2 | Group 9
15
Planned waypoint route (XY)
Start
1
2
3
4
Goal
Controller starts at (−3.0, 0) and follows 5 waypoints toward (2.15, 0).
1
GPS + encoders
Estimate position and wheel motion
2
Waypoint heading
Compute target angle and speed
3
LiDAR obstacle check
Turn if front range < 0.65 m
4
Motor commands
Differential-drive wheel speeds
5
Logging
Save all sensors and camera frames

## Slide 16
Q4
Q4(a) Slip estimation and experiment logs
Longitudinal slip is computed from encoder and GPS velocity; every trial saves synchronized sensor data
MAS512 | Assignment 2 | Group 9
16
Longitudinal slip estimate
slip = (v_enc − v_x) / v_x
v_enc = 0.1 · (ω_left + ω_right) / 2
Computed only when |v_x| ≥ 0.05 m/s.
Recorded devices
GPS · accelerometer · gyro · IMU
Left/right encoders · left/right motors
Camera snapshots every 12 steps
LiDAR range array every simulation step
Outputs per friction condition
sensors.csv
GPS XY, distance, wheel speed, slip, IMU
lidar.jsonl
Timestamped LiDAR ranges
camera/
Recorded PNG images
summary.json
Goal reached, time, distance, clearance

## Slide 17
Q4
Q4(b–c) Friction experiment results
Higher wheel–floor friction greatly reduces measured longitudinal slip
MAS512 | Assignment 2 | Group 9
17
Key results
3 baseline trials (μ = 0.12) and 3 higher-friction trials (μ = 1.0).
6/6 runs reached the stopping area near the target.
Mean |slip| dropped by 94.8%.
Condition summary
Condition
Mean |slip|
Duration [s]
Distance [m]
Baseline
6.7622%
28.3520
7.248
High friction
0.3515%
27.9093
7.176
94.8% reduction
Trajectory coloured by slip

## Slide 18
Assignment 2 — Summary and conclusions
What we implemented and measured across camera, LiDAR, fusion and Webots
MAS512 | Assignment 2 | Group 9
18
Q1
Camera geometry
889/900 YOLO detections; 70 depth corrections; R² = 1.0 mapping
Camera intrinsics need correct image resolution
Q2
LiDAR motion
99/99 load centroids; 0.785 m Y span; ≈ 0 sensor motion
KISS-ICP tracks sensor pose, not the moving load
Q3
Sensor fusion
4/5 KITTI box associations; mean range difference 1.82 m
Small five-frame sample; range surfaces differ
Q4
Webots experiments
6 successful Webots runs; mean absolute slip fell from 6.76% to 0.35%
Higher friction reduced slip by 94.8% while keeping path length and duration almost unchanged